FREERDP
SOFTWARE DESIGN

By
Marc-André Moreau
Jay Sorg

January 2010

# 1. FreeRDP

## 1.1 Overview

One of the biggest changes in FreeRDP compared to rdesktop is the effort that has been put to make FreeRDP more modular and closer to the design of Microsoft's mstsc.exe client. FreeRDP is not a single program, but a set of programs and libraries for the RDP protocol. Here is a diagram showing the major components forming FreeRDP:

# 2. libfreerdp

## 2.1 Overview

libfreerdp is the core of FreeRDP. It should be as portable as possible, with most of the operating system specific code being in the other components of FreeRDP. It's goal is nothing more but to provide a client library for the remote desktop protocol. One of the major design flaws of rdesktop is that there is no such library, meaning that there is no clean separation of the code implementing RDP and the code for the X11 interface, making it hard to make user interfaces using libraries other than X11, and also harder to port to other platforms.
## 2.2 Core

The core of the protocol is implemented in rdp.c. This is where data is received and sent at the RDP layer. Received PDUs are dispatched to the different parts of libfreerdp that handle them.
## 2.3 Capabilities

All capability sets have been implemented in capabilities.c, in compliance to [MS-RDPBCGR].

# 3. libkbd
## 3.1 Keyboard Input Systems

# 4. xfreerdp

## 4.1 Overview